## Slide 1
We’ve Got
Your Back!
The 10 most common misconceptions many cleaners have about chemistry and equipment which are costing them time and money

## Slide 2
We’ve Got
Your Back!
Thanks for coming – fill out your entry from to be registered for the drawing

## Slide 3
We’ve Got
Your Back!
Download for today’s presentation
Powerpoint presentation
Links to support material for further investigation and study
Product application assistance
Located at: https://hydramaster.com/presentation-download
/
If you have a smartphone or tablet with you, feel free to download it now and follow along

## Slide 4
Resources (for further investigation)
https://thecleansceneblog.wordpress.com/2017/03/02/myths-fables-fact-about-vacuum-science/?frame-nonce=85f72963f9
https://thecleansceneblog.wordpress.com/2014/02/13/carpets-health-and-science-a-new-understanding-for-the-residential-and-commercial-carpet-owner-2/?frame-nonce=85f72963f9
Berry, Dr. Michael, “Characteristics of High-Performance Carpet Cleaning”, The Journal of Cleaning, Restoration, and Inspection, IICRC, Winter 2017, pages 20-26
http://digitaledition.qwinc.com/publication/index.php?i=377830&m=&l=&p=1&pre=&ver=html5#{"page":20,"issue_id":377830}
Berry, Dr. Michael A, Protecting the Built Environment – Cleaning for Health, TriComm 21st Press, Chapel Hill, NC, 1993

## Slide 5
Resources (for further investigation)
Press release on the Airmed study: http://www.prweb.com/releases/2013/2/prweb10470656.htm\;
Detailed information on the study: http://press.shawinc.com/wp-content/uploads/2014/01/Shaw_Phase_I_Study.pdf and http://press.shawinc.com/wp-content/uploads/2013/12/Shaw_Phase_II_Study.pdf
http://www.shawcontract.com/Content/LiteraturePDFs/Technical_pdf/carpetsinschools02.pdf
https://thecleansceneblog.wordpress.com/2013/10/30/the-value-of-heat-in-extraction-cleaning/?frame-nonce=ac45bada5c
https://thecleansceneblog.wordpress.com/2013/11/16/the-7-most-common-misconceptions-about-carpet-cleaning-chemistry-part-1/?frame-nonce=ac45bada5c

## Slide 6
Resources (for further investigation)
https://thecleansceneblog.wordpress.com/2013/11/18/tthe-7-most-common-misconceptions-about-carpet-cleaning-chemistry-part-2/?frame-nonce=ac45bada5c
https://thecleansceneblog.wordpress.com/2013/11/20/the-7-most-common-misconceptions-about-carpet-cleaning-chemistry-part-3/?frame-nonce=ac45bada5c
https://thecleansceneblog.wordpress.com/2013/11/22/the-7-most-common-misconceptions-about-carpet-cleaning-chemistry-part-4-of-7-by-doyle-bloss/?frame-nonce=ac45bada5c
https://thecleansceneblog.wordpress.com/2013/11/26/common-misconceptions-about-carpet-cleaning-chemistry-part-5-of-7/?frame-nonce=ac45bada5c
https://thecleansceneblog.wordpress.com/2013/12/02/common-misconceptions-about-carpet-cleaning-chemistry-part-6-of-7/?frame-nonce=ac45bada5c

## Slide 7
Resources (for further investigation)
https://thecleansceneblog.wordpress.com/2013/12/03/common-misconceptions-about-carpet-cleaning-chemistry-part-7-of-7/?frame-nonce=ac45bada5c
(http://www.newton.dep.anl.gov/askasci/gen01/gen01759.htm)
https://hydramaster.com/cleaning-guides/
http://apps.appmachine.com/cleanmaster

## Slide 8
We’ve Got
Your Back!
1. More Does Better. Boosting is always better.
We’ve Got
Your Back!
Any sweeeeeeet tea drinkers here?

## Slide 9
We’ve Got
Your Back!
1. More Does Better. Boosting is always better.
Concentrated formulas max out their cleaning power
They are as concentrated as the solution allows
When you “overmix” – at best you are wasting money; at worst you leave behind a sticky residue.

## Slide 10
We’ve Got
Your Back!
1. More Does Better. Boosting is always better.
Most boosting solutions are already in your high powered presprays;
sodium carbonate;
d’ Limonene;
sodium percarbonate;
hydrogen peroxide;
butyl solvent or one if it’s safer and environmentally friendlier replacements

## Slide 11
We’ve Got
Your Back!
1. More Does Better. Boosting is always better.
When boosting to get a chemical reaction – usually effervescence – the chemical reaction has a short shelf life.
Oxidized oils (such as asphalt oil tracking) often do respond better to last second boosting with oxidizers

## Slide 12
We’ve Got
Your Back!
1. More Does Better. Boosting is always better.
Choose the right solution for the soiling and traffic conditions, consider the fiber, and you should normally not need to boost if you select the right solution.
Agitation does more than boosting. If you are cleaning a lot of carpets you think you need boosters on, try a CRB machine first and maximize your cleaning solution temperature

## Slide 13
We’ve Got
Your Back!
More Does Better. Boosting is always better.
Product Application

## Slide 14
We’ve Got
Your Back!
2. When and how do you measure pH when it comes to potential effects on carpet?
Requirements or recommendations for using a specific pH range? Is that concentrated or diluted (ready-to-use)?
On first glance, it makes sense you are concerned about the immediate interaction of a high (or low) pH ready to use solution on the carpet or fiber you are cleaning
Buffering?
What about the residue you leave behind?

## Slide 15
2. When and how do you measure pH when it comes to potential effects on carpet?
Product Application

## Slide 16
3. Are hard surface floors really better for people with allergies and asthma?
If carpet acts as a filter and collects dust and pollutants and germs and allergens, then what does a hard surface floor do?
CRI sponsored studies said, “wait a minute” but they are biased right?
Sweden began removing carpet from government controlled facilities more than 30 years ago.

## Slide 17
3. Are hard surface floors really better for people with allergies and asthma?
Study by the Swedish Institute of Fiber and Polymer Research:
  1973, 15 million square meters of carpet – allergy complaints = about 1 million people
  1990, 5 million square meters of carpet – allergy complaints = 3.5 million people

## Slide 18
3. Are hard surface floors really better for people with allergies and asthma?
Study by the Swedish Institute of Fiber and Polymer Research:
  1973, 15 million square meters of carpet – allergy complaints = about 1 million people
  1990, 5 million square meters of carpet – allergy complaints = 3.5 million people

## Slide 19
3. Are hard surface floors really better for people with allergies and asthma?
2010 study by the Airmid Health Group:
  Built nine different floor plans inside a test chamber – one room with hard surfaces, the other 8 with various types of carpeting
  Allergen test dust was applied to all floor surfaces. The rooms were allowed to equilibrate overnight before testing began. Then, after normal room disturbances and cleaning, airborne particulate counts as well as surface and allergen measurements were undertaken for each room type.

## Slide 20
3. Are hard surface floors really better for people with allergies and asthma?
2010 study by the Airmid Health Group: Results?
After performing their tests, among the conclusions the researchers reached are the following:
Different floor coverings have a significant impact on airborne particle concentration (which can potentially cause allergic reactions).
In general, airborne particle concentrations were lower with carpet as opposed to the hard-surface floor.
The pile height of the carpet and carpet fiber composition influenced the particulate retention capacity of the carpets.
Carpet made of 100 percent nylon medium pile height broadloom consistently performed best in terms of low levels of airborne allergens.
The results tell us that the carpets, especially 100 percent nylon carpets which are a common type, acted as a reservoir, capturing and trapping allergens and reducing airborne allergen levels overall in the rooms when compared to the hard-surface floor. In other words, the carpets would help reduce allergic reactions, not cause them.

## Slide 21
3. Are hard surface floors really better for people with allergies and asthma?

## Slide 22
3. Are hard surface floors really better for people with allergies and asthma?
While the researchers concluded that carpets do help protect health overall, they added that in order for carpets to continue doing this, they must be properly maintained.
As to the use of steam or water-based cleaning systems, the researchers suggest carpet extraction—and more specifically hot-water carpet extraction—is necessary to thoroughly clean carpets and remove deeply embedded soils and contaminants, helping to prevent them from becoming airborne. According to the researchers, “results show that the proprietary hot water extraction cleaning process was highly effective in reducing allergen levels in carpets and soft furnishings. Surface levels of dust mite allergens on carpets, for example, were reduced by 91 percent, of cat allergen by 95 percent, and of dog allergen by 97 percent. The cleaning process also resulted in a marked reduction in airborne cat allergen exposure. The process also effectively reduced exposure to airborne mold.”

## Slide 23
3. Are hard surface floors really better for people with allergies and asthma?
Product Application

## Slide 24
4. Which is better for your customer – low residue cleaning or “good” residue cleaning?
We’ve Got
Your Back!
No residue,
Low residue,
Good residue,
Bad residue.

## Slide 25
We’ve Got
Your Back!
4. Which is better for your customer – low residue cleaning or “good” residue cleaning?
Soil is anything foreign to the construction of the carpet – there is no such thing as a completely residue free carpet –anytime

## Slide 26
We’ve Got
Your Back!
4. Which is better for your customer – low residue cleaning or “good” residue cleaning?
Let’s find common ground on just exactly what is bad residue?
  The more soil extracted and removed – the better.
  Chemical residue that physically abrades carpet fiber or chemically attacks the fiber or the backing is bad.
  Residue left behind that is sticky and can cause rapid re-soiling is bad
  Residue that could encourage biological growth is bad

## Slide 27
We’ve Got
Your Back!
4. Which is better for your customer – low residue cleaning or “good” residue cleaning?
So we are left with two choices – which is better?
  Good residue left behind after the carpet cleaning is completed (for example – anti-resoiling polymers)
  OR
  Leaving behind the least amount of total residue
It depends upon when you got into the industry and who trained you
  Indoor environmental quality – scientific studies of the 90’s and 2000’s
  OR
  Encapsulation and polymers

## Slide 28
We’ve Got
Your Back!
4. Which is better for your customer – low residue cleaning or “good” residue cleaning?
You can’t claim to be a low residue cleaner while simultaneously claiming you leave behind stuff in the carpet that helps the carpet stay cleaner longer – Can you?
  Do polymers break down into respirable particulates?
  Would residual anti-microbials left in carpet reduce allergens and bacteria and mold growth and …
Physical extraction and removal of soil (all soil)
makes for a healthier environment

## Slide 29
4. Which is better for your customer – low residue cleaning or “good” residue cleaning?
Product Application
Low Residue
Polymer

## Slide 30
5. Does acid rinsing leave less residue than using an extraction detergent?
  What solution do you run through your extraction equipment?
  Acid rinse
  Detergent acid rinse
  Fresh water rinse
  Alkaline detergent solution
  Modified or energized water

## Slide 31
We’ve Got
Your Back!
5. Does acid rinsing leave less residue than using an extraction detergent?
  What do we know?
  None are automatically more or less likely to cause re-soiling – pH of residue is not linked to re-soiling
  Definition of residue or soil revisited
  You can measure by weight
  CRI SOA measurements
In testing, alkaline rinsing leaves the least amount of residue likely because it removes more soiling

## Slide 32
We’ve Got
Your Back!
5. Does acid rinsing leave less residue than using an extraction detergent?
Product Application
Alkaline Extraction Detergent Rinse
Alkaline Extraction Detergent FREE Rinse
Acid (Neutralizing) Detergent Rinse
Acid Detergent FREE Rinse

## Slide 33
We’ve Got
Your Back!
6. Is wool carpet harder to clean than a synthetic carpet?
Grandma’s house
So why all the hullaballoo?
Wool is very absorbent – needs help drying
Wool rugs vs wool carpet
Jute backing in wool carpets – shrinkage and browning – and the good ol’ portable days
Wool is expensive
Where do the sheep go when it rains?
Been to Vegas? Wool is NOT wimpy

## Slide 34
We’ve Got
Your Back!
6. Is wool carpet harder to clean than a synthetic carpet? – The cleaning “rules”
Wool should not be cleaned with carpet cleaning formulations that contain optical brighteners.
Wool can be damaged by prolonged exposure to oxidizing bleaches. Wool smells really bad when exposed to reducing bleaches.
Both reducing agents and oxidizing agents in a carpet cleaning solution can cause bleaching or alteration of carpet colors
Wool should not be cleaned with a total alkalinity that is too alkaline.

## Slide 35
We’ve Got
Your Back!
6. Is wool carpet harder to clean than a synthetic carpet? – The cleaning “rules”
Wool exposed to high alkalinity over an extended period of time or repeated applications can damage the epidermis of the wool fiber, resulting in felting
Wool should not be cleaned with temperatures greater than 160 degrees Fahrenheit.
The carpet cleaning solution should not alter or affect the flammability rating of the carpet.
The carpet cleaning solution should not contain any agents which lead to rapid re-soiling of the carpet after cleaning because they leave behind some sticky or soil attracting residue.

## Slide 36
We’ve Got
Your Back!
6. Is wool carpet harder to clean than a synthetic carpet? – Conclusion?
Wool is a fabulous carpet fiber. It is soft. It wears well. It is naturally flame resistant. It is sustainable and renewable. It cleans up effectively when properly maintained on a periodic basis. It is NOT wimpy, or delicate, or hard to clean. A trained and thoughtful cleaning professional always practices reasonable caution when cleaning any carpet. Don’t be afraid of wool carpet! Embrace it as the high end carpet that it is. Clean it with confidence.

## Slide 37
6. Is wool carpet harder to clean than a synthetic carpet?
Product Application
We’ve Got
Your Back!
Residential Wool Carpet and Rug Prespray
Commercial Wool Carpet Prespray
Acid Detergent
Rinse
Acid Rinse

## Slide 38
We’ve Got
Your Back!
7. Does a higher pH and more solvents get a dirty polyester carpet cleaner?
Polyester has overtaken nylon as the #1 selling residential carpet fiber
It is oil-loving and water repelling
So what is a cleaner to do when it gets really dirty and he/she is expected to resurrect it? – MORE POWER!
Your favorite prespray for trashed carpets uses high pH and a large amount of solvents
Your CRI SOA certified product had to pass non-resoiling testing criteria
Surfactants can be the most “sticky” part of a carpet cleaning solution

## Slide 39
We’ve Got
Your Back!
7. Does a higher pH and more solvents get a dirty polyester carpet cleaner?
You need a solution that can penetrate the water repelling tendencies of the carpet and dissolve the oil
You need a solution that has been tested for soil removal with a test soil that includes an oily component on polyester carpet, not nylon
Acid rinsing does not make much sense with a dirty polyester carpet

## Slide 40
We’ve Got
Your Back!
7. Does a higher pH and more solvents get a dirty polyester carpet cleaner?
Product Application
Olefin/Polyester Formulated and Tested Prespray
Olefin/Polyester Alkaline Detergent Extraction Rinses

## Slide 41
We’ve Got
Your Back!
8. Bigger is always better when it comes to truckmounts

## Slide 42
We’ve Got
Your Back!
8. Bigger is always better when it comes to truckmounts

## Slide 43
We’ve Got
Your Back!
8. Bigger is always better when it comes to truckmounts

## Slide 44
2016 Industry Survey Results
Vacuum
Reliability
Temperature
?
8. Bigger is always better when it comes to truckmounts

## Slide 45
1. What are and will be your main uses for your truckmount?
Carpet Cleaning
Upholstery Cleaning
Hard Surface Cleaning – Stone ▪ Tile ▪ Concrete
Flood Extraction/Water Damage Restoration
Pressure Washing?
8. Bigger is always better when it comes to truckmounts

## Slide 46
2. What types of jobs will you be doing?
Commercial – Class A
Commercial
Residential
8. Bigger is always better when it comes to truckmounts

## Slide 47
3. Thinking about your last month’s jobs, how much vacuum hose do you normally use (Hose pull length)?
100-149’
150 – 200’
200’ +
8. Bigger is always better when it comes to truckmounts

## Slide 48
4. What do you value most?
Performance
Reliability
Price
8. Bigger is always better when it comes to truckmounts

## Slide 49
5. Who is going to be working on the machine for service and maintenance? How mechanical are you? How far are you from a service center?
8. Bigger is always better when it comes to truckmounts

## Slide 50
6. Have you ever done dual wand cleaning? Do you anticipate doing a lot of dual wand cleaning in the future?
Yes
No
Maybe
8. Bigger is always better when it comes to truckmounts

## Slide 51
7. How are you going to make the investment?
Have financing in place
Need financing help
Paying cash
8. Bigger is always better when it comes to truckmounts

## Slide 52
8. What van are you planning on putting the machine in?
New van
  Chevy/GMC Cargo
  Ford Transit
  Dodge ProMaster
  Nissan
Used Van
Trailer
8. Bigger is always better when it comes to truckmounts

## Slide 53
What are they (perhaps, you?) really wanting?
Vacuum Blower Size
Reduce customer carpet drying times
Fuel consumption considerations
Blower longevity
Longer hose runs
8. Bigger is always better when it comes to truckmounts

## Slide 54
What are they (perhaps, you?) really wanting?
Heat (Solution Temperature)
Faster cleaning
Reduce drying times
Reduce chemical usage
Reduce microorganisms
8. Bigger is always better when it comes to truckmounts

## Slide 55
What are they really (perhaps, you?) wanting?
Pressure (Solution Pressure)
How much pressure are you going to consistently need?
300-450 psi
800-1200 psi
2000 psi +
8. Bigger is always better when it comes to truckmounts

## Slide 56
What are they really wanting?
Engine (Power)
Adequate without too high of rpm’s
Adequate without overkill
Bigger equals more fuel consumption
Liquid cooled or air cooled
Direct Drive / PTO
8. Bigger is always better when it comes to truckmounts

## Slide 57
9. More CFM is the end all, be all to vacuum performance and faster drying carpets
Myth #1: The more lift a system has, the better the cleaning will be
Myth #2 The more CFM a vacuum has, the drier the carpet will be after cleaning.
Myth #3: Vacuum Pressure reading on the vacuum gauge represents the entire load on the machine.

## Slide 58
10. The temperature gauge on my machine says 220°F, so that is what temperature I am cleaning the carpet at.
“Lie Detectors”
Du Pont Study
Consistent delivery of hot solution

## Slide 59
We’ve Got
Your Back!
Come by and see us
Booth #310, 303
Outside Booth #1001, 1003

## Slide 60
We’ve Got
Your Back!

## Slide 61
We’ve Got
Your Back!

## Slide 62
We’ve Got
Your Back!

## Slide 63
We’ve Got
Your Back!
Thank you for attending.
Enjoy the beach.